## Slide 1: Operating Systems and Architectures CSCM98, Lecture 2: Programs, Processes and Threads
Benjamin Mora
1
Swansea University
Dr. Benjamin Mora

## Slide 2: Content
Role of the Kernel.
Processes & Threads.
Loading and Linking.
Interrupts.
Examples in C (Thread and Process creation) and C++11.
2
Benjamin Mora
Swansea University
Notes: Possibly quickly discuss event programming and multi-processor as well

## Slide 3: OS Kernel
3
Benjamin Mora
Swansea University

## Slide 4: Role of the Kernel
The Kernel implements all the necessary tools for an Operating System to run and manage the computer.
  A collection of programs that are executed with OS privileges.
A big focus on Inputs/Output (I/O) and managing resources.
  Drivers.
Kernel code is protected from user.
Sometimes refers to a program linked to a System Call or a specific action.
  Kernel Modules
4
Benjamin Mora
Swansea University

## Slide 5: Role of the Kernel
System calls are often made by applications/programs.
  E.g., print a message on screen.
  Application not necessarily involved (e.g., exception).
  These calls are handled by the OS in Kernel space (i.e., kernel or supervisor mode).
  As opposed to User space.
System calls are usually slow and should be minimized.
  Requires context switching.
  Calling thread is put on hold.
Implementing concurrency may require many system calls (Creation, synchronization & communication) !!!
5
Benjamin Mora
Swansea University

## Slide 6: Monolithic Kernels
6
Benjamin Mora
Swansea University
Application(s)
Device Drivers
Hardware
Scheduler, Virtual memory
IPC
File System
System call
User mode
Kernel mode
Protection level

## Slide 7: Monolithic Kernels
Monolithic Kernels implement all the different components of an OS, but with some dependencies.
Difficult to implement as the OS and its functionalities grow.
  A bug in kernel mode can compromise the entire system.
Micro-Kernels have been developed as a solution.
7
Benjamin Mora
Swansea University

## Slide 8: Micro Kernels
8
Benjamin Mora
Swansea University
Application(s)
Micro-Kernel (Basic IPC, Virtual Memory and Scheduling )
Hardware
…
User mode
Kernel mode
Privileges/
Protection level (Ring)
Device Drivers
File Server
Virtual Memory
Ring 2 or 3
Ring 0
Notes: Only Ring 0 applications can access crucial elements of the hardware directly.

## Slide 9: Micro Kernels
Benefits:
  Uniform Interfaces.
  Flexibility.
  Reliability.
  Portability.
  Extensibility.
  …
Lower Performances.
  Communications done by message passing.
Micro Kernel Modules or Services can be easily loaded without reboot or rebuilding the kernel.
9
Benjamin Mora
Swansea University
Notes: Extend notion of rings and user modes!

## Slide 10: Micro Kernels
Ring 3:
User Mode
Ring 1 & 2:
Device Drivers
Rings:
  Protection at different levels.
  Prevents code to get access to resources outside of their scope of application (Sandboxing).
X86 processors have 4 levels of protection.
Supported by the Hardware (processor)
  Would be too slow otherwise.
  2 bits for a page description.
  For instance, a web applet should not get control of
  your webcam as it is running in user-mode
  (ring 3, least privilege).
10
Benjamin Mora
Swansea University
Ring 0:
Kernel
Notes: Extend notion of rings and user modes!

## Slide 11: Processes
11
Benjamin Mora
Swansea University

## Slide 12: Introduction to Processes: Topics
Program Life span/Process definition.
Program vs Process.
Code execution.
Java threads.
Process memory.
Stack & Call stack.
Processes and Threads.
Process states.

## Slide 13: Program vs machine code vs Binary
13
Benjamin Mora
Swansea University
");

## Slide 14: Program vs machine code vs Binary
Program
  Evolves as you write it!
Machine code
  From the compilation of your program!
  Or from interpretation (e.g., Java virtual machine)
  Store on disk as a program.
Binary code
  A binary representation of the machine code interpretable by processor.

## Slide 15: Program lifespan
15
Benjamin Mora
Swansea University
Source Code, High Level Language
Compiled or Interpreted Code
(.exe, Java PCode, etc…)
Compilation/Interpretation
Runable program
Program Loaded by OS. Creation of context.
Process running
Execution by CPU
Additional threads running
Possible creation of new threads

## Slide 16: CPU and Code execution
i=i+1;
16
Benjamin Mora
Swansea University
R1
R2
ALU
SP
PC
Registers
Stack Pointer and Program Counter
CPU
Memory
i
3
MOV R1, i
ADD R1, #1
MOV i, R1
4
3
4
Notes: Yellow: Program
Pink:Data

## Slide 17: CPU and Code execution
The execution of a program is mainly sequential.
  Only a single basic instruction at a time (single processor).
    Well, not so true for modern processors …
      Multithreading.
Operating systems are multi-tasked while some processors have a single core. How is it possible to execute two different codes simultaneously ?
  Real-Time code interleaving is obviously not possible.
  One strength of the OS is its ability to quickly switch between different programs.
17
Benjamin Mora
Swansea University
Task 1
t
Task 2
Task 1
…

## Slide 18: Processes & Threads: Simple Java Example
18
Benjamin Mora
Swansea University
//WorkingThreads Extends Thread
//WorkerRunnable implements Runnable
Notes: Possibly quickly discuss event programming and multi-threading as well

## Slide 19: Simple Java Example
19
Benjamin Mora
Swansea University

## Slide 20: Simple Java Example
20
Benjamin Mora
Swansea University

## Slide 21: Simple Java Example
21
Benjamin Mora
Swansea University

## Slide 22: Output
22
Benjamin Mora
Swansea University
Workers started
Hello from worker B
Hello from worker A
Worker B exiting
Worker A exiting
Workers finished

## Slide 23: Or possibly (!)
23
Benjamin Mora
Swansea University
Hello from worker B
Workers started
Hello from worker A
Worker A exiting
Worker B exiting
Workers finished

## Slide 24: Process vs Program
A process is an instance of a Program running.
  A process is not a program!
  A Process is dynamic.
  The program is fixed at compilation time, before running it.
  The same program can be run several times, creating as many processes:
    1 powerpoint.exe file!
    Many PowerPoint windows!
  Processes do not usually share memory space and are isolated from each other.

## Slide 25: Processes and Threads
A thread is similar to a process, but usually shares memory with other threads.
  The difference is made when instantiating (i.e., creating) the process/thread (See later).
  Groups of threads usually share (the virtual) memory space and can access each other’s memory.
  They must have a common thread/process ancestor.
  Separate memory stacks!
    Memory stack mainly used to store local variables of a function.
25
Benjamin Mora
Swansea University

## Slide 26: Memory From a Process Point of View Process Image
26
Benjamin Mora
Swansea University
Process Control Block
Program
Heap (Data)
Global variables &
dynamically allocated memory
Stack
Top of Stack
Logical Address
(virtual memory)
Local Variables for current function call

## Slide 27: The memory Stack: Storing local variables Example: A recursive function
Memory Stack
int PowerOfTwo(unsigned int n)
{
if (n==0)
return 1;
else return
2*PowerOfTwo(n-1);
}
…
PowerOfTwo(3);
27
Benjamin Mora
Swansea University
PowerOfTwo: 3
PowerOfTwo: 2
PowerOfTwo: 1
PowerOfTwo: 0
return: 1
return: 2
return: 4
return: 8
program
Thread’s Stack

## Slide 28: Memory Stack
Stores local variables
  As a function can be called at any time (non-deterministically).
  Is duplicated for each thread/process.
Changes dynamically
  Push/pops operations.
  Returned values are pushed onto the stack.
Has limited size.
  Large variables should be dynamically allocated on most systems/with most languages.

## Slide 29: Memory From a Process Point of View
Function Calls as handled by programs & processors:
  Push arguments and return address onto the stack.
  Jump to function code address (PC register).
  Execute Function.
  Push Result onto the stack.
  Jump Back.
Specific hardware acceleration on processors.
29
Benjamin Mora
Swansea University

## Slide 30: Processes and Threads
Multi-tasks operating systems quickly swap the different processes that are running on a computer (Pseudo-parallelism).
To do so, some information related to the process must be stored by the OS.
  The Process Control Block (PCB) stores different attributes related to the process. This is a fundamental data structure!
  The Process Image consists of a memory block (Heap), the code to be executed, one or many thread stacks, and the PCB.
All processes are stored in a process table.
30
Benjamin Mora
Swansea University

## Slide 31: Process Control Block
Identifiers:
  Unique Process identifier (Usually an integer).
  Parents and Children process identifiers.
  User identifier.
CPU registers need to be saved during a context switch:
  Registers, program counter, stack pointer, flags, etc…
Scheduling and State information:
  Process state, priority, resources used…
31
Benjamin Mora
Swansea University

## Slide 32: Context Switching
Context Switching swaps the current process(es) running on the CPU.
How does it work ?
easy solution:
  Save current process state.
  Load a new process state.
32
Benjamin Mora
Swansea University

## Slide 33: Context Switching
Well not so easy!
States:
  Register content => Written to memory!
  Memory => Page table modified!
  I/O ports => Kernel data structure updated!
Determining the new process to be run is called Scheduling!
  Details will come later!
33
Benjamin Mora
Swansea University

## Slide 34: Remember Java Threads
34
Benjamin Mora
Swansea University
Notes: From a User point of view

## Slide 35: Process States: 5-state model
35
Benjamin Mora
Swansea University
Notes: From an Operating System point of view

## Slide 36: Process States
Running.
  The process is running on the CPU.
Ready.
  The process could use a CPU if one were available.
Blocked.
  The process is waiting for some event (typically a completion of an I/O request).
Suspended Ready.
  The process is swapped out to secondary storage, waiting to be resumed.
Suspended Blocked.
  The process is swapped out to secondary storage, waiting either for some event, or to be resumed.
36
Benjamin Mora
Swansea University

## Slide 37: Process States
Having a two or three state model is possible as well.
  Less efficient.
  Virtual memory is better handled with 5 states.
There is usually a process queue associated with every state.
  Scheduling will be see later.
37
Benjamin Mora
Swansea University

## Slide 38: Process Creation
By loading a specified program:
  Creation of a new process.
  Loading of the program.
  Activation of the process.
By duplication from a parent process (fork function under UNIX):
  A new process is created.
  All the parental data is usually inherited (copy).
    Including stack.
  A hierarchy of process is then possible.
    Killing a process will also usually kill its children.
  May take a huge number of cycles.
38
Benjamin Mora
Swansea University

## Slide 39: Inter-Process Communication (IPC)
Communication between processes is often wished.
  Parallelized algorithms.
  Multithreaded programs.
There are several ways to make processes communicate (detailed later in the course).
  Signals.
  Pipes (and files).
  Shared memory.
  Message passing.
  Remote Procedure Calls.
  Sockets.
  MPI (not really seen here)
  …
39
Benjamin Mora
Swansea University

## Slide 40: Threads
40
Benjamin Mora
Swansea University

## Slide 41: Thread Creation
Very similar to processes, but:
  A process can “contain” many threads.
  The threads have access to the same memory data as the parent process, but each thread gets its own stack (processes also get a stack).
Benefits:
  Creation is then much faster.
  Inter-Process Communication is easy.
    Inter-Thread Communication actually!
    Though we must be careful when doing so.
41
Benjamin Mora
Swansea University

## Slide 42: Relationships between threads and processes (OS Specific)
Threads : Processes
  1:1
    Each thread is a unique process (UNIX)
  M:1
    A process has both a defined address space and resources. (Windows, Linux, etc…)
  1:M
    A thread can migrate from one process to another (Ra (clouds), Emerald).
  M:N
    Combines the last two cases. (TRIX, IBM NGPT)
42
Benjamin Mora
Swansea University
Notes: 1:1 more or less
More expensive context Switch => picture

## Slide 43: Threads
Lightweight processes (kernel threads).
Shared memory.
  Same address space.
  Global variables are the same.
Separate stack.
  Local variables are usually different.
Faster creation.
43
Benjamin Mora
Swansea University
Notes: Quick reminder 1 running code, 1 processor.
Role of the Stack

## Slide 44: Two Types of threads
User threads:
  The kernel (E.G., OS) is not aware of any thread, and is only involved in the management of the parent process.
  Everything related to the thread management is done by the program itself, without any call to kernel subroutines.
    Scheduling.
    Communications.
  Requires a thread library.
44
Benjamin Mora
Swansea University
Notes: Mention blocking system calls is a problem…
Running in non-privileged code
User space
M:1 P167 stallings\

## Slide 45: Two Types of threads
User threads:
  No kernel mode privileges.
    Save 2 mode switches.
  Context switching only involves loading/saving CPU registers.
  Scheduling can be application specific.
  Several threads can be in a running mode at the same time.
    Well only one get the cpu at a given time…
45
Benjamin Mora
Swansea University
Notes: User space
M:1 P167 stallings\

## Slide 46: Two Types of threads
User threads:
  System calls are an issue.
    OS (Kernel) invoked.
    Blocking other threads.
  Jacketing.
    Blocking calls become non-blocking calls.
    Try again later instead of waiting.
  Threads can only be run on a single CPU/core.
46
Benjamin Mora
Swansea University
Notes: User space
M:1 P167 stallings\

## Slide 47: Two Types of threads
Kernel threads:
  Managing threads is done by the system scheduler itself.
  An Application Programming Interface (API) must be used by the programmer.
  Thread switching can be slower.
  Available on most systems.
47
Benjamin Mora
Swansea University
Notes: 1:1 more or less
More expensive context Switch => picture

## Slide 48: Loading & Linking
48
Benjamin Mora
Swansea University

## Slide 49: Loading & Linking
Let’s imagine a single line of (C) code:
  static int variable;
How is this variable located at run-time?
  (address binding)
49
Benjamin Mora
Swansea University
File.c
Libraries
Compilation
File.o
}
Linker
Module
Loader
Memory
Process
Process Address

## Slide 50: Loading & Linking
The compiler cannot always know in advance where the program and its data will be located.
  Symbolic addresses used instead in assembly code.
The loader charges the program in memory.
  Absolute loading: Module always located at the same place.
    Real address in RAM.
  Relocatable loading: Handle addresses relative to the starting point of the module.
    The norm on a modern computer.
50
Benjamin Mora
Swansea University
Notes: Add Magic Numbers

## Slide 51: Loading & Linking
Different types of Linking after compilation:
  Static linking.
    Duplicate specific libraries.
    Must be available at compilation time.
  Dynamic linking.
    One instance of the library running.
    Updates can be done to libraries without recompiling program!
    May save library by handling only once instance of code for all the running programs.
    An update may break your program though if your program does not respect specs or if a bug has been introduced.
51
Benjamin Mora
Swansea University

## Slide 52: Interrupts
52
Benjamin Mora
Swansea University

## Slide 53: Interrupts
An interrupts is a CPU mechanism to help with the parallelization of tasks.
When an interrupt is raised, the mechanism is usually as follows:
  The current program state is saved (including CPU registers) in order to be able to continue the program execution later on.
  The appropriate Interrupt handler (i.e., a specific program) is called.
53
Benjamin Mora
Swansea University

## Slide 54: Interrupts
Different types of interrupts:
  I/O devices such as I/O completion, I/O errors and I/O ready.
  Disks for buffered disk access.
  Network devices for network communications.
  Machine errors (or machine check) such as power cut, hardware failure, etc.
  Timer. Expiration of a given amount of time.
  Terminals, such as interrupt key, restart key, etc.
  Software interrupts. Caused by execution of a particular machine instruction.
  Traps/Exceptions such as division by zero, arithmetic overflow, …
  Supervisor call. Occurs (on some systems) when a running process requires a system call.
54
Benjamin Mora
Swansea University

## Slide 55: Interrupts : Exceptions.
Faults:
  Must be fixed before current instruction.
    E.g., page fault.
Traps:
  Must be fixed after instruction.
    E.g., Breakpoint, overflow , divide-by-zero.
    Switch to kernel mode.
Abort:
  E.g., is_computer_on_fire() system call.
  Not recoverable.
  Not handled exception, exception in exception
55
Benjamin Mora
Swansea University

## Slide 56: Interrupt Priorities: Example
Power Failure. Level 8.
Hardware traps. Level 7.
Clock. Level 6.
Keyboard. Level 5.
Serial I/O. Level 4.
Disk Driver. Level 3.
Tape Driver. Level 2.
Printer. Level 1.
Software interrupts. Level 0.
56
Benjamin Mora
Swansea University

## Slide 57: Interrupts Levels
An interrupt can be interrupted by another interrupt only if the new one is of higher level.
An interrupt vector/table is associated with the interrupts. For each level corresponds an entry in the table. The entry is usually just a pointer to the routine in charge of processing the interrupt.
57
Benjamin Mora
Swansea University

## Slide 58: Programming With Threads in C++11
58
Benjamin Mora
Swansea University

## Slide 59: Background
C++11, C++14, C++17
  Moved C++ into new programming concepts.
Many new components part of the language:
  Threads
  Mutexes
  Units
  Etc..
59
Benjamin Mora
Swansea University

## Slide 60: Thread Creation
Very Simple from C++11 on (or java)!
void threadCode(int id) {
std::cout << "Hello World from " << id << std::endl;
}
int main() {
//Launch a thread
std::thread t (threadCode,1);
//Join the thread with the main thread
t.join();
return 0;
}
60
Benjamin Mora
Swansea University

## Slide 61: Programming Processes and Threads in C: Quick Overview
61
Benjamin Mora
Swansea University

## Slide 62: Background
POSIX library for UNIX environments.
  Portable Operating System Interface.
Many “non-native” Functionalities:
  Threads
  Mutexes
  Signals
  Pipes
  Etc..
62
Benjamin Mora
Swansea University

## Slide 63: Processes: UNIX Fork Example
main() {
  int pid;
  pid=fork();
  switch (pid) {
  case -1: printf(“An error has occurred\n”); break;
  case 0: printf(“I am the child process\n”); break;
  default: printf(“My child is %d\n”, pid); break;}
}
Possible output result on stdout
I am the child process
My child is 1234
63
Benjamin Mora
Swansea University
Notes: Fork not so common anymore. Clone() command. Stdout described later

## Slide 64: Processes: Wait function
int wait(int *status);
Force the parent process to wait for a child to stop or terminate.
  returns -1 if an error has occurred.
  Returns the PID of the child process that ended otherwise.
  The exit status is passed to the argument.
The wait command can be useful as it does not waste CPU resources (process puts on hold).
64
Benjamin Mora
Swansea University

## Slide 65: Processes: Running External Commands
Exec functions:
  execl, execv, execle, execv, execvp.
  Allows running a new command from the program.
  The current process image is replaced by the new one.
  The exec function call never returns unless if running the new command has failed.
Prototypes:
  int execlp(const char *file, const char *arg, ...);
  int execv(const char *path, char *const argv[]);
  …
65
Benjamin Mora
Swansea University

## Slide 66: POSIX Threads (PThreads)
Originally, there were as many thread libraries as there were UNIX systems.
IEEE standardized it with POSIX threads in 1995.
  Ease portability.
Also known as PThreads.
  #include <pthread.h>
  Compilation: -pthread option
66
Benjamin Mora
Swansea University

## Slide 67: POSIX Threads in C : A Typical Use
pthread_exit
pthread_exit
67
Benjamin Mora
Swansea University
pthread_create
Thread 1 running
Thread x running
…
pthread_barrier_wait
pthread_barrier_wait
…
pthread_join
One thread merges intermediate results
pthread_barrier_wait
pthread_barrier_wait
…
Thread 1 running
Thread x running
…
pthread_barrier_init
pthread_barrier_destroy
Called x times

## Slide 68: Creating a new thread
int pthread_create (
pthread_t *thread,
const pthread_attr_t *attr,
void (*start_routine)(void*),
void *arg);
The first argument (thread) returns the thread attributes at the address pointed by thread.
The second argument (attr) represent the attributes needed for the thread creation.
  NULL can be used for using default attributes.
68
Benjamin Mora
Swansea University

## Slide 69: Creating a new thread
int pthread_create (
pthread_t *thread,
const pthread_attr_t *attr,
void (*start_routine)(void*),
void *arg);
Third attribute represents the starting point function.
  Takes a void* argument.
  Can be seen as the thread’s “main”.
arg represents a pointer to a possible list of arguments.
  Up to the programmer to decide how to use it!
  Can also be used to pass a single (casted) integer value!
Returned value is either 0 (OK) or the error code.
69
Benjamin Mora
Swansea University

## Slide 70: Exiting a Thread
void pthread_exit(void *value_ptr);
value_ptr can be used to return a value to any code waiting for the termination.
In the main process, pthread_exit must be called (instead of exit or return) before its termination.
  If not, the threads that are still running shall be killed as well.
pthread_join
  Wait for a specific thread completion.
70
Benjamin Mora
Swansea University

## Slide 71: Example:
#include <stdio.h>
#include <pthread.h>
void *message(void *arg) {
printf(“%s\n”,((char *) arg));
pthread_exit(NULL);
}
main() {
  pthread_t attrib[2];//….
  pthread_create (attrib, NULL, message, (void *) “Child #1”);
  pthread_create (attrib+1,NULL, message, (void *) “Child #2”);
pthread_exit(NULL);
}
71
Benjamin Mora
Swansea University
Result:
child #2
child #1
Notes: Add barriers

## Slide 72: Barriers:
#include <stdio.h>
#include <pthread.h>
int nbProcess=4;
Barrier initialization before running some threads…
pthread_barrier_t barrier;
pthread_barrier_init(&barrier, NULL, nbProcesses);
Then call wait inside a running thread whenever suitable…
pthread_barrier_wait(&barrier);
Destroy barriers when not needed anymore. After pthread_join…
pthread_barrier_destroy(&barrier);
72
Benjamin Mora
Swansea University