## Slide 1: Operating Systems and Architectures CSCM98, Part 5: Introduction to CPUs
Benjamin Mora
1
Swansea University
Dr. Benjamin Mora

## Slide 2: Content
Transistors and Gates
Registers and Arithmetic units
CPU Pipeline
SIMD Programming

## Slide 3: Transistors and Logical Gates
CPUs are made of transistors
These transistors allow creating logical gates like a NAND gate.
3
Benjamin Mora
Swansea University
From http://cpuville.com/logic_gates.htm
Donn Stewart 2010
A NAND gate

## Slide 4: Truth Tables
Implemented with Logical gates
4
Benjamin Mora
Swansea University
A
0 1
0
1
and
0 0
0 1
A
0 1
0
1
or
0 1
1 1
A
0 1
0
1
nand
1 1
1 0
A
0 1
0
1
nor
1 0
0 0
A
0 1
0
1
xor
0 1
1 0
B
B
B
B
B

## Slide 5: Simple Adder
Logical gates can be combined to create circuits like adders, multipliers, etc…
A 1-bit and 4-bit adders
http://http://en.wikipedia.org/wiki/Adder_(electronics)
Adders can be combined to create n-bits adders (e.g. 32-bit adder, etc).
  Multipliers, comparators, tests
  More specialized: bit counts, random number generators, etc…
5
Benjamin Mora
Swansea University
Notes: Carry missing in the 1-bit adder

## Slide 6: Advanced Adder
There are various ways to implement circuits
Kogge–Stone adder (S=A+B, better than previous design):
http://en.wikipedia.org/wiki/Kogge%E2%80%93Stone_adder
Depth of circuit is important (delay/latency)
  And so the number of links (complexity).
  And so the maximum distance (signal propagation: latency).
6
Benjamin Mora
Swansea University
Bits … S4 S3 S2 S1 S0
… A2,B2 A1,B1 A0,B0

## Slide 7: Implementing Arithmetics in Hardware
Precomputed tables are often implemented in circuits
  Shorter latency (just one lookup is needed in the table)
    Simplicity (not in term of transistors, but only design).
  Limited precision (e.g., 4x4 bit tables)
    Does not scale well and requires many transistors.
    Use of several iterations (e.g., Newton-Raphson) to get full precision.
  Good for implementing specific, difficult circuits.
    MUL, DIV, RSQRT (1/Sqrt(x)), RCP (1/x).
7
Benjamin Mora
Swansea University

## Slide 8: Registers
What is a program?
8
Benjamin Mora
Swansea University
i=i+1
R1
R2
ALU
SP
PC
Registers
Stack Pointer and Program Counter
CPU
Memory
i
3
Mov R1, i
Add R1, #1
Mov i, R1
4
3
4
Notes: Or
i = i+1
i <- i+1

## Slide 9: A Modern processor
9
Benjamin Mora
Swansea University
Memory
Mov R1, i
Add R1, #1
Mov i, R1
R1
R2
ALU
SP
PC
L1 Data
Cache
Instruction
Cache
Prediction
Cache
TLB
Cache
L2 Data
Cache
L3 Data
Cache
R1
R2
ALU
SP
PC
L1 Data
Cache
Instruction
Cache
Prediction
Cache
TLB
Cache
L2 Data
Cache
R1
R2
ALU
SP
PC
L1 Data
Cache
Instruction
Cache
Prediction
Cache
TLB
Cache
L2 Data
Cache
R1
R2
ALU
SP
PC
L1 Data
Cache
Instruction
Cache
Prediction
Cache
TLB
Cache
L2 Data
Cache
CPU
Core #1
Memory
Bus
Notes: Or
i = i+1
i <- i+1

## Slide 10: CPU Pipelines
10
Benjamin Mora
Swansea University
http://www.anandtech.com/show/6936/intels-silvermont-architecture-revealed-getting-serious-about-mobile/2
Notes: More detailed stages

## Slide 11: Decoding a Program
The program counter points to the instruction that is currently executed, and then moves to the next one at the next clock cycle unless a (possibly conditional) jump instruction is encountered.
Circuits (adder, etc…) deal directly (and only) with registers, not memory.
Instructions must be scheduled!
  Pipeline(d).
  Fetch, decode, Execute, write-back stages.
Requires many transistors for scheduling.
Instructions have latencies and throughput associated.
11
Benjamin Mora
Swansea University

## Slide 12: Instructions’ Latency and Throughput (X86)
MUL,FMUL,ADD,FADD,SUB,FSUB:
  Usually 1 or 2 instructions completed per clock cycle.
    Latency of 5 for FMUL.
    Really depends on design (processor generation), circumstances (data in caches) and dependencies (if/while instructions).
DIV,FDIV: 10 to 20 clock cycles latency.
IF THEN ELSE (branching instructions)
  0/1 cycle if well predicted by CPU (additional transistors)
  ~10 to ~20 if mispredicted or no branch prediction hardware available (Discussed later)
12
Benjamin Mora
Swansea University

## Slide 13
13
Benjamin Mora
Swansea University
http://www.anandtech.com/show/6355/intels-haswell-architecture/8

## Slide 14: Intructions’ control flow optimizations
The flow of instructions (Scheduling) should be kept continuous.
  Ideally one or several instructions executed per clock.
  8 execution ports on Intel’s Haswell (e.g., i7 4770K)
    14-stage pipeline, 168-entry register file.
      Notion of register has become more logical than physical as they are actually renamed and implemented as a buffer.
Difficult (or more complex):
  Branching conditions.
  Instruction dependencies.
    Out-of-order execution
  Instructions should be loaded and decoded first
    Caches needed
14
Benjamin Mora
Swansea University

## Slide 15: Power Consumption and Multicore
CPU
Power consumption of chips does not increase linearly with frequency in general!
  Power = Frequency x Voltage2
Solution is to go multicore.
  Scales better… provided that algorithms and code do.
15
Benjamin Mora
Swansea University
Core 0
L1 cache
Core 1
L1 cache
Core 2
L1 cache
Core 3
L1 cache
L2 cache
L2 cache
L2 cache
L2 cache
L3 cache
Memory

## Slide 16: Wafers
16
Benjamin Mora
Swansea University
http://www.bbc.co.uk/news/technology-19557496

## Slide 17: CPU’s SIMD Units
Single Instruction Multiple Data
1 instruction to schedule several computations of the same type.
  Different from VLIW ! (Very Long Instruction Word)
  Can be 4-wide (MMX, SSE, NEON), 8-wide (AVX), 16-wide and more (GPUs)
  Can accelerate by as much math operations.
Saves transistors and complexity!
  1 operation to be scheduled only.
  1 address translation only (see MMU later on)
Several constraints, not all algorithms can easily benefit from SIMD execution units.
  Scaling with wide(r) units may be an issue.
17
Benjamin Mora
Swansea University

## Slide 18: SIMD Units: Principles
18
Benjamin Mora
Swansea University
3
5
2
3
8
2
5
6
1
2
7
1
4
7
2
3
1
3
4
1
3
2
8
6
0
0
6
1
8
1
3
1
4
8
6
4
11
4
13
12
1
2
13
2
12
8
5
4
A
B
C
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=

## Slide 19: Traditional C program
int A[16] = {3,5,2,3,8,2,5,6,1,2,7,1,4,7,2,3};
int B[16] = {1,3,4,1,3,2,8,6,0,0,6,1,8,1,3,1};
int C[16];
//16 adds!
for (int i=0;i<16;i++)
C[i]=A[i]+B[i];
19
Benjamin Mora
Swansea University

## Slide 20: SIMD Units: Principles
20
Benjamin Mora
Swansea University
3
5
2
3
8
2
5
6
1
2
7
1
4
7
2
3
1
3
4
1
3
2
8
6
0
0
6
1
8
1
3
1
4
8
6
4
11
4
13
12
1
2
13
2
12
8
5
4
A
B
C
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
Per-lane operations !

## Slide 21: SIMD Units: Principles
21
Benjamin Mora
Swansea University
3
5
2
3
8
2
5
6
1
2
7
1
4
7
2
3
1
3
4
1
3
2
8
6
0
0
6
1
8
1
3
1
4
8
6
4
11
4
13
12
1
2
13
2
12
8
5
4
A
B
C
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
Let’s suppose 32-bit integers (int, 4 bytes). For a given architecture, one can fix a computational block/packet size.
What we can have for 64 bytes:
  2 blocks of 32 bytes (=8 ints per block, AVX width)!
  4 blocks of 16 bytes (SSE width, 4 ints per block)!
Notes: Usually, an int declarations gives you a 4-byte signed integer, but not always!

## Slide 22: AVX Coding Using AVX intrinsics
int A[16] = {3,5,2,3,8,2,5,6,1,2,7,1,4,7,2,3};
int B[16] = {1,3,4,1,3,2,8,6,0,0,6,1,8,1,3,1};
int C[16];
//Type casting, No real operation involved.
__m256i *ptA=(__m256i *) A;
__m256i *ptB=(__m256i *) B;
__m256i *ptC=(__m256i *) C;
//Only two instructions as 8 operations are carried out in one //instruction!
ptC[0]=_mm256_add_epi32(ptA[0],ptB[0]);
ptC[1]=_mm256_add_epi32(ptA[1],ptB[1]);
22
Benjamin Mora
Swansea University
Notes: Missing is a 32-byte alignment of the arrays! Compiler could do it, but it is 16-byte align usually.
Could be 32 operations at a time on bytes.
Intrinsics are pseudo functions matching the hardware specifications, and that tell the compiler to use the hardware instruction when compiling.

## Slide 23: SIMD Principles
__m256i represents a 32-byte "array" of integer “nature”.
  __m256 for float types.
  __m256d for double types (only 4 elements).
_mm256_add_epi32 adds 8 signed 32-bit integers!
  epi8, epi16 & epi64 may exist for some instructions
    E.g., adding to 16-bit integers
23
Benjamin Mora
Swansea University

## Slide 24: 1 AVX Register (256 bits/32 bytes)
24
Benjamin Mora
Swansea University
float
float
float
float
float
float
float
float
0
1
2
3
4
5
6
7
Bit 0
Bit 256
double
double
double
double
0
2
3
1
short
0
1
2
3
4
5
6
7
short
short
short
short
short
short
short
short
short
short
short
short
short
short
short
8
9
10
11
12
13
14
15

## Slide 25: SIMD Principles
What do you get with 32-byte (not bits) registers?
  4 double precision floating point values (double)
  8 single precision floating point values (float)
  8 32-bit integers (int, signed or not)
  16 16-bit integers (short, signed or not)
  32 8-bit integers (char, signed or not)
25
Benjamin Mora
Swansea University
Notes: Standard sizes for C-types, but not in C specs nor a requirement.

## Slide 26: SIMD Principles
Most instructions work on a per-lane basis!
  Atomicity ensured!
Elements must be consecutively stored in memory and then loaded in a register for processing.
Not all operations are possible!
  Binary operators (e.g., AND OR XOR ), MUL, ADD, MIN, MAX, FSQRT, DIV,RCP are quite common operators.
  Some cross lanes operations exist!
26
Benjamin Mora
Swansea University

## Slide 27: SIMD Principles
Use of intrinsics (pseudo-assembly with types) saves us from typing tedious assembly code.
  Intrinsics-based code can be improved with some #defines
  #define add8i(a,b) (_mm256_add_epi32((a),(b)))
    c=add8i(a,b)
27
Benjamin Mora
Swansea University

## Slide 28: Examples of AVX2 instructions
AVX 1 does not support integer operations!
  epi8 (char), epi16 (short), epi32 (int), ps (float) are AVX2 extensions.
  pd (double).
  In-lane examples (specs):
  __m256 _mm256_and_ps(__m256 m1, __m256 m2);
  __m256 _mm256_or_pd(__m256 m1, __m256 m2);
  __m256 _mm256_div_ps(__m256 m1, __m256 m2);
  __m256i _mm256_and_epi32(__m256i m1, __m256i m2);
  __m256 _mm256_min_ps(__m256 m1, __m256 m2);
  __m256 _mm256_max_ps(__m256 m1, __m256 m2);
  __m256 _mm256_rsqrt_ps(__m256 m1);
  __m256i _mm256_abs_epi32(__m256i s1);
28
Benjamin Mora
Swansea University
Notes: ps: floating point
epi32 32-bit signed integers

## Slide 29: Examples of AVX2 instructions
Special operation: shuffling floating point content:
  __m128 _mm_shuffle_ps(__m128 a , __m128 b , const int i );
  __m256 _mm256_shuffle_ps(__m256 a , __m256 b , const int i );
29
Benjamin Mora
Swansea University
3
8
2
5
1
4
6
7
3
2
4
6
A
B
C
c = _mm_shuffle_ps (a,b,0x98); //0x98 = 0b 10 01 10 00 SSE inst., not AVX
00 01 10 11
00 01 10 11
00 01 10 11

## Slide 30: Examples of AVX2 instructions
The shuffle instruction picks two elements of A and two elements of B.
It requires a const code for blending the two vectors.
AVX 8-wide version only works on two 4-wide sub-arrays, and data cannot cross the middle lane.
Permute instruction to be used as well for AVX instructions!
  Different from the previous shuffle instruction!
  extern __m256 _mm256_permute2f128_ps
  (__m256 m1, __m256 m2, int control);
Benjamin Mora

## Slide 31: AVX Permute instruction
Benjamin Mora
3
5
2
3
8
2
5
6
1
3
4
1
3
2
8
6
3
5
2
3
3
2
8
6
A
B
C
00 01
10 11
  C= _mm256_permute2f128_ps(A,B, 0x30);
0x30=0b00110000
00 01
}
}

## Slide 32: Why do we need shuffling instructions?
To do horizontal operations in several steps
  i.e., not per lane operations (unsupported).
Example: fast horizontal min
  Removes branching tests!
Also, fast matrix transpose!
Benjamin Mora
3
8
2
5
A
00 01 10 11
8
3
5
2
B
3
3
2
2
A
B=shuffle(A,A,0xE4)
A=min(A,B)
2
2
3
3
B
B=shuffle(A,A,0x1B)
2
2
2
2
A
A=min(A,B)

## Slide 33: Examples of AVX instructions
_mm256_min_ps(…)
  1 clock cycle throughput
  Much better than:
  if (a>b) c=b else c=a;
    Because of a test (branch)!
    Because of multiple instructions.
    (Good) compilers can sometimes detect and optimize this C code!
Benjamin Mora

## Slide 34: SIMD instructions: Prefetching
Not having data close to the processor is an issue!
Usually around ~50 clock cycles to access memory!
  vs. ~1 instruction per clock cycle usually (throughput)
  Difference/delay is not acceptable.
    Cache(s) will minimise the problem.
  Using any data (e.g. an int variable) in code often requires at least one load and so prefetching was invented...
Benjamin Mora
3
5
2
3
8
2
5
6
…
2
7
1
4
7
2
3
Processing order
Process here
Prefetch here
Prefetch distance

## Slide 35: SIMD instructions: Prefetching
Prefetch instruction:
  void _mm_prefetch(char * p , int i );
  i variable for specifying which cache is concerned.
Automatic prefetching done by modern processors
  Slightly less efficient.
  Mainly loading adjacent cache lines.
Prefetch distance depends on the case.
Make sure you do not prefetch a non valid cache-line.
  Not allocated, not written memory area!
  Typically end of array!
Benjamin Mora
Notes: Prefetching prefetches a full line of cache (64 aligned bytes) around the pointer address (which points to a specific byte!). i can be set to for instance _mm_hint_t0 to specify the Level 0 cache, i.e. the one closest to the processor.

## Slide 36: Other useful SIMD instructions
Streaming stores
  Bypass L2 and L3 caches without polluting them.
    See lecture on caches.
    E.g. void _mm_stream_ps(float * p , __m128 a );
    (SSE instruction)
Getting masks (i.e., highest bits)
  extern int _mm256_movemask_ps(__m256 a);
  int B= _mm256_movemask_ps(A);
Benjamin Mora
-0.3f
1.f
-5.f
2.f
10.f
-1.f
-1.f
1.f
0
1
2
3
4
5
6
7
A
B=0b01100101=64+32+4+1=99

## Slide 37: SIMD instructions: Prefetching
Streaming stores improve bandwidth when dealing with large streams of data (read once, write once).
movemask instructions allow on integer to store some binary state about a full SIMD register
  Can be used with other instructions like bitcount instructions or lookup tables.
  E.g., counting how many positive values contained inside an SIMD register.
  E.g., Radix sort.
Benjamin Mora

## Slide 38: Other useful SIMD instructions
Integer/Float conversions
Random Number Generation (AVX 2)
  E.g., _rdrand32_step(unsigned int *)
Encryption/Decryption
  AES-128
    40 steps
  AES-192
    48 steps
  AES-256
    56 steps
Benjamin Mora
Notes: __m256 __cdecl _mm256_i32gather_ps(float const *, __m256i, const int );

## Slide 39: Other useful SIMD instructions
Gather/Scatter operations.
Gather implemented in AVX2
__m256 __cdecl _mm256_i32gather_ps
(float const *, __m256i, const int );
Returns 8 floats packed in an AVX register from a float address and 8 32-bit indices.
i.e. computing v=A[i] in parallel.
Throughput still low!
Benjamin Mora

## Slide 40: Other useful SIMD instructions
String: Packed comparisons (introduced with SSE 4.2)
Sum of absolute differences
  For image compression
  __m128i _mm_mpsadbw_epu8( __m128i a, __m128i b, const int mask );
Reciprocal, RSQRT
  Requires a Newton-Raphson iteration for better precision (22 bits).
  Fast implementation.
Benjamin Mora

## Slide 41: Data Structures and memory Linearity (C)
typedef struct { float x; float y; float z;} Point;
Point myPoints[2];
x
y
z
x
Point #0
y
z
Point #1
Memory address
Notes: The way data is stored is crucial to understand when it comes to optimizations. Memory bandwidth is one of the most limiting factors and should be carefully thought about. This is especially important when dealing with SIMD units

## Slide 42: SIMD Programming: Data Structures
Structures need to be aligned for best performances!
  16-byte (SSE) or 32 bytes (AVX)
Arrays of Structures VS Structures of Arrays!
  AoS vs SoA
  Example: A set of 3D points:
Benjamin Mora
x
y
z
x
AoS
Point #0
y
z
x
y
z
x
y
z
x
y
x
…
Point #1
Point #2
…
x
y
z
x
y
z
NA
x
NA
x
y
x
…
…
y
z
NA
NA
or
SoA
x
y
z
x
y
z
x
y
z
x
y
z
…
…
…
#0
#1
#2
#3
…

## Slide 43: SIMD Programming: Data Structures
Structures of Arrays better at handling:
  Read-only data
  Processed in large consecutive chunks
Arrays of Structures better at handling:
  Reconfigurable data
  More random access patterns (never a good thing)
    Due to increased cache locality.
  Often requires extra operations (like a transpose) to put things back in order.

## Slide 44: SIMD Programming: Data Structures
Intermediate representation can be useful sometimes
  Array of Structures of Arrays (AoSoA)
x0
x1
x2
Point #0
…
x3
y0
y1
y2
y3
z0
z1
z2
z3
x4
x5
x6
x7
Notes: Prefetching prefetches a full line of cache.
(i.e. 4-wide SIMD, R1: XXXX, R2:YYYY, R3:ZZZZ)

## Slide 45: IEEE floating-point representation
1 float representation (32 bits used)
X=(-1)s(1+M)2E-127
Benjamin Mora
1
0
0
1
1
0
0
1
1
0
0
1
0
0
0
1
0
0
0
1
1
0
0
0
0
0
0
0
1
0
0
1
Sign
Exponent
Mantissa

## Slide 46: IEEE floating-point representation
Absolute Value without branching
float x=…;
unsigned int abs=0x7FFFFFFF;
x=x & ((float &) abs);
Works well with SIMD instructions!
  Explains why AVX2 abs (absolute value) instruction implemented in hardware for integers, but not for floating point values.
Benjamin Mora

## Slide 47: IEEE floating-point Representation
Benjamin Mora
float myFunction( float number )
{
long i; float x2, y;
const float threehalfs = 1.5F;
x2 = number * 0.5F;
y = number; i = * ( long * ) &y;
// evil floating point bit level hacking
i = 0x5f3759df - ( i >> 1 ); // what the fuck?
y = * ( float * ) &i;
y = y * ( threehalfs - ( x2 * y * y ) );
// 1st iteration
// y = y * ( threehalfs - ( x2 * y * y ) );
// 2nd iteration, this can be removed
return y;
}
Quake 3 Arena code (Wikipedia).
Any idea about what it does?
Notes: http://en.wikipedia.org/wiki/Fast_inverse_square_root
John Carmack evil Fast inverse square root implemented in Quake3!

## Slide 48: Further Reading
Verilog.
VHDL.
Various Circuit designs.
48
Benjamin Mora
Swansea University

## Slide 49: Other topics seen separately
Transactional memory.
Cache.
TLB
MMU
Cache trashing.
49
Benjamin Mora
Swansea University